# Counter Heating Display

# Operation instructions

HHV1130

CAUTION:

Read the instructions before using the machine.

Dear Customer,

Congratulations on your purchase of this product.

Please take a few minutes before starting operation of the appliance and read the

following operating instructions.

Many thanks.

Table of Contents

2. Table of Contents

3. Safety

4. Safety

5. General

5. Structure and Parts

6. Preparation and Power Supply

6. Installation and operation

7. Maintenance and cleaning

8. Cautions

8. Major Parameters

8. Electric Circuit Diagram

Safety

※ The appliance is not to be used by persons (including children) with reduced physical, sensory or mental capabilities, or lack of experience and knowledge, unless they have been given supervision or instruction.

※ The maximum weight of the empty appliance is 43 kg.

※ The appliance is only intended for commercial and indoor use by trained and skilled personnel familiar with these instructions.

WARNING: If the appliance is positioned adjacent to other areas or appliances, it is recommended that, within the range of the radiation, these areas or appliances be made of non-combustible material, otherwise, they shall be clad with a non-combustible heat-insulating material, and attention is to be paid to fire prevention regulations.

※ Children being supervised not to play with the appliance.

※ This appliance can be used by children aged from 8 years and above and persons with reduced physical, sensory or mental capabilities or lack of experience and knowledge if they have been given supervision or instruction concerning use of the appliance in a safe way and understand the hazards involved.

※ Children shall not play with the appliance.

※ Cleaning and user maintenance shall not be made by children without supervision

※ If the supply cord is damaged, it must be replaced by the manufacturer, its service agent or similarly qualified persons in order to avoid a hazard.

※ Don't use any kind of pressure water jet for cleaning the device.

To prevent hazards and to ensure optimum efficiency, no modifications or alterations to the device that are not explicitly approved by the manufacturer may be undertaken.

※ This device may only be operated in technically proper and safe condition.

※ The device should be never left unattended during operation. Keep away children.

※ Preserve this manual safely. When passing on/selling the device to a third party, the manuals must be handed over along with the device.

※ Every person using the device must act in accordance to the manuals and under consideration of the safety advice.

※ The device is to be used indoors only.

※ Any technical interventions, as well as assembly and maintenance are to be made by a qualified customer service only.

Caution hot sunface.

Do not put the food direct contact with the shelf.

General

1. This instruction manual contains information about the installation, operation and maintenance of the device and should be consulted as an important source of information and reference guide.

2. Awareness of the safety instructions and instructions for use in this manual will ensure the safe and correct use of the device.

Structure and Parts

Preparation and Power Supply

Exclusive power socket

The power receptacle must have a reliable earth connection.

No share on socket

Never let the device share the common socket with other appliance, otherwise the cable becomes hot and fire might be resulted.

Protect cables

Never break or damage the cables otherwise current leakage and fire might be resulted.

No water flushing

Never give the device surface a flush otherwise current leakage might be resulted.

Prevent from flammables and explosive

Never put any flammable or explosive inside the device such as ether, gasoline, alcohol, adhesive and explosive. Never put dangerous product nearby the device.

Installation and Operation

Installation

- Place the device on top of an even and safe surface which supports the weight of the device and is not heat sensitive.

- Not at any time should you place the device on an inflammable surface (such as table cloth, carpet,etc)

- You must no position the device near open fireplaces, electric ovens/arc furnaces/electric heaters or other heat sources.

- Position the device in such a way that the plug is easily accessible.

Operation

- Before first use, clean the inner sides and the playing grids with a soft cloth and a mild cleaning agent.

Afterwards, dry the device thoroughly.

- Remove the water bowl from the device. The water bowl is installed inside the device and then fill the water bowl with water.

- Connect the power power plug to a suitable electrical outlet with protective ground. Power on the appliance with main switch.

- Set the temperature as required for respective foods. You may adjust the desired temperature in the range between 30℃-90℃.

- The temperature inside of the hot display can be read from the front display.

- Put the foods in appropriate containers before playing them inside the hot display and shut is by using the sliding door.

- Some of the device parts become very hot, always use safety gloves when placing or removing foods.

- The foods are kept warm at the temperature set by you previously.

- In order to place or remove foods. You may open the door at rear side.

- Switch on the inner light when required using the light switch of the device.

- Disconnect the device from the power socket when the device is not in use.

Cleaning and Maintenance

- Before beginning with repair or cleaning  works make sure the device has been disconnected from the power socket and has cooled sown.

- Don’t  use any acid agents and make sure no water ingresses the device,

- To protected yourself from the electric shock, never immerse the device, its cables and the plug in water or other liquids.

- Don’t use any kind of pressure water jet for cleaning the device.

Cleaning

- The device should be cleaned regularly.

- Clean the device from the inside and outside with a soft, damp cloth and a mild cleaning agent.

- Clean the placing grids and the housing with a soft, damp cloth and a mild cleaning agent.

- Clean the water bowl regularly. Calcification at the water bowl may be removed with common agents or liquids.

- Only use a soft cloth and make sure you never use any kind of abrasive agents or pads which could scratch the surface.

- After the cleaning procedure, you should use a soft and dry cloth to wipe dry and polish the surface.

- Make sure the device has been cleaned properly before storing it in a dry place.

Maintenance

- Check the mains lead from time to time to ensure it is not damaged in any way. Never use the device if the lead is damaged. If the lead is damaged, it must be replaced by a qualified electrician.

- Only a qualified technician should carry out repairs and maintenance of the device, Do not attempt to repair the device by yourself.

- Appliances must be disconnected from their power supply during cleaning or maintenance and when replacing parts.

Cautions

Children should be supervised to ensure that they do not play with the appliance.

- If the supply cord is damaged, it must be replaced by the manufacturer, its service agent or similarly qualified persons in order to avoid a hazard.

Major Parameters

| Model Parameter | HCV1130 |
| --- | --- |
| Temperature range(ºC) | 30-90 |
| General Rated input power(W) | 1500 |
| Rated current(A) | 6.3 |
| Rated voltage(V) | 220-240~ |
| Rated frequency(Hz) | 50 |
| Storage Volume(L) | 130 |
| Net weight (kg) | 43 |
| Grade of Waterproof | IPX4 |
| Overall Dimension(mm) | 856x568x686 |
| Lamp power(W) | 2.5(LED) |

Circuit Diagram

Note

- The electric circuit diagram and parameters on the product name plate are final ones if they have been changed.

- The  design might be improved without notice.

Meaning of crossed out wheeled dustbin:

Do not dispose of electrical appliances as unsorted municipal waste,use separate collection facilities.

Contact you local government for information regarding the collection systems available.

If electrical appliances are disposed of in landfills or dumps, hazardous substances can leak into the groundwater and get into the food chain, damaging your health and well-being.

When replacing old appliances with new ones, the retailer is legally obligated to take back your old appliance for disposals at least free of charge.

QA18-0000002599

Disposal

Environmental Protection

Discarded electric appliances are recyclable and should not be discarded in the domestic waste! Please actively support us in conserving resources and protecting the environment by returning this appliance to the collection centres.

Dispose of packaging in accordance to applicable legal regulations.

WARRANTY

A statutory warranty applies for this product.

Damages caused by wrong treatment or operation, by false placement or storage, improper connection

or installation, as well as force or other external influences are not covered by this warranty. We

recommend careful reading of the operating instructions as it contains important information.

Note:

- In case this product does not function correctly, please firstly check if there are other reasons, e.g. for electrical appliances interruption of the power supply, or generally incorrect handling are the cause.

- Please note that, where possible, the following documents or rather information should be provided together with your faulty product:

- Purchase receipt

- Model description/Type/Brand

- Describe the fault and problem as detailed as possible

In the case of a claim for guarantee or defects, please contact the seller.

QA18-0000002599

MCC Trading International GmbH

Schlüterstr. 5

40235 Düsseldorf

Germany

Made in China (for packaging and IM)

GWL 8/14 EN                                                                                                                                                   ENGLISH

# Text boxes

Glass door

Water Bowl

Shelf

Lamp Cover

Temperature Display

Shelf Bracket

Power receptacle

Earth bar

Self-resetting

thermal cut-out

Thermostat

Heating Element

220-240V~

60Hz

Indicator Lamp

LED Lamp

Non self-resetting

thermal cut-out